## Slide 1
How indoor readings reach an application
AM300 SENSOR + UG65 GATEWAY
01
Four components carry one reading from the room to the screen.
AM300
Measures indoor
conditions
Exact model determines
which parameters it measures.
UG65
Receives radio
messages
Forwards sensor messages
through its IP connection.
Network server
Sessions and
message routing
Controls joining and routes
uplinks to an integration.
Cloud / app
Uses the sensor
readings
Decodes, stores or displays
data, depending on platform.
LoRaWAN radio
IP backhaul
Integration
Model check
AM304L, AM305L, AM307, AM308/AM308L and AM319 can measure different parameters. Confirm the unit label and matching guide.
Notes: Follow one reading from the room sensor to the screen. These are logical roles. A gateway is a radio-to-IP bridge and is not automatically a dashboard or network server. AM300 models and firmware can differ, so identify the full model before choosing units and decoder. The sensor sends compact LoRaWAN uplinks at configured intervals or for events. The UG65 listens on configured channels. Multiple gateways may hear the same uplink. Milesight advertises up to 2,000 devices, 8-channel communication and up to 2 km urban coverage for UG65. These are maximum product figures, not guarantees for a particular site. Confirm regional hardware, firmware and manuals.
Source: user-provided AM300 Sensor and UG65 Gateway outline, slides 1, 2, 4 and 5. Supplied references: https://www.milesight.com/iot/product/lorawan-sensor/am300 and https://www.milesight.com/iot/product/lorawan-gateway/ug65.

## Slide 2
Frontend dashboard and system flow
Presents current readings, historical charts and alerts to users.
AM300 SENSOR + UG65 GATEWAY
02
AM304L sensor
Measures indoor conditions
UG65 gateway
Receives radio messages
Network server
Device authentication
Message processing
LoRaWAN over LoRa
IP packet forwarding
MQTT or HTTP
Backend app
Validation, rules
and alerts
Database
Sensor readings
and alert history
Store and retrieve
Frontend
Readings, charts
and alerts
HTTP/HTTPS API requests
Sensor data and alert responses
Dashboard responsibilities
Current environmental readings
Historical measurement charts
Sensor and connection status
Threshold exceedances
Alert history for staff
Possible technologies
HTML, CSS, JavaScript
or React
Notes: The frontend displays current environmental readings and historical measurements in charts. It shows sensor and connection status, highlights readings that exceed configured thresholds, and provides alert history and relevant information for staff. Possible technologies include HTML, CSS, JavaScript or React. The architecture is a logical design supplied by the user. AM304L sends LoRaWAN over LoRa radio to UG65. The gateway uses IP networking and packet forwarding to the LoRaWAN network server. The server integrates with the backend through MQTT or HTTP, depending on configuration. The backend stores and retrieves database records. The frontend sends HTTP/HTTPS API requests to the backend, and the backend responds with sensor data and alerts. The dashboard does not directly query the database in this diagram.
Source: user-provided section 3.6 and Mermaid flowchart.

## Slide 3
Protocols and decoding
AM300 SENSOR + UG65 GATEWAY
03
LoRaWAN carries the sensor message. MQTT and APIs can deliver it downstream.
AM300
Binary payload
UG65
Radio to IP
LoRaWAN
IP forwarding
Network server
Routes uplinks
Platform-specific routes
MQTT publisher
Publishes to a broker
MQTT broker
App subscribes
REST API / webhook
Cloud service or app/API client
Payload decoding
A decoder for the exact model converts sensor bytes into readings.
The platform may then provide JSON. Raw data may be hex or Base64.
Notes: Diagram shows alternative downstream integrations, not a guaranteed feature path for every gateway or platform. UG65 forwards over an IP connection using its configured mode. Ask which component runs the decoder and which publishes to MQTT or exposes an API. MQTT uses a broker. An API is a software interface, often over HTTP. Neither is the AM300-to-UG65 radio link. JSON is a data format, not a protocol. The sensor uses model-specific compact binary payloads. A platform can offer decoded JSON after decoding, while other messages may contain raw hex or Base64. Milesight documents REST APIs and webhooks for its Development Platform. Confirm any direct UG65 API/MQTT feature against the exact gateway manual and firmware. Optional building-system connections can use BACnet or Modbus when configured.
Source: user-provided outline, slides 3 and 6. Supplied references: https://www.milesight.com/iot/resources/download-center/ and https://github.com/Milesight-IoT/SensorDecoders.

## Slide 4
Backend application
Processes sensor data and manages the rules that create alerts.
AM300 SENSOR + UG65 GATEWAY
04
INPUT
Sensor data from the network server
Receive and decode
Receive messages.
Decode payloads
when necessary.
Validate
Check readings
and timestamps.
Apply rules
Evaluate configured
thresholds and
generate alerts.
Store and serve
Store readings and
alerts. Provide data
through an API.
OUTPUT
Validated readings, stored records and alert information
The frontend requests data through the backend API.
Notes: Purpose: process and manage sensor data. Receive data from the network server. Decode the application payload if necessary. Validate readings and timestamps. Apply configured threshold rules. Generate alerts when defined conditions are met. Store readings and alert information in the database. Provide data to the frontend through an API. Input: sensor data from the network server. Output: validated readings, stored records and alert information.
Source: user-provided section 3.4.

## Slide 5
Database
Stores sensor readings and alert information for historical analysis.
AM300 SENSOR + UG65 GATEWAY
05
POSSIBLE RECORD CONTENT
Information group | Fields to store
Identity and location | Device ID, room or sensor location
Measurement | Type, value and unit
Time | Timestamp
Device health | Device status
Alerts | Alert status and alert history
Technology options
PostgreSQL
or InfluxDB
Choose according to project requirements.
The backend stores and retrieves these records.
Notes: Purpose: retain sensor data for historical analysis. Possible fields include device ID, room or sensor location, measurement type, value and unit, timestamp, device status, alert status and alert history. PostgreSQL and InfluxDB are possible technologies, not a finalized selection. Choose according to the project requirements. The backend stores and retrieves the data.
Source: user-provided section 3.5 and Mermaid architecture.